Architectural and engineering specifications

S6LP

• The 2-way full range passive loudspeaker system shall have one direct radiating neodymium magnet, 1.5-inch voice coil, 6-inch low frequency transducer and and one 1-inch voice coil diameter, PEN  diaphragm neodymium magnet compression driver loaded onto a horn. Low frequency transducer shall be rated at a nominal impedance of 8 ohm for S6LP/8 model or at a nominal impedance of 16 ohm for S6LP/16 model. High frequency transducer shall be rated at a nominal impedance of 8 ohm (nominal impedance).

• The usable bandwidth shall be 63Hz to 20kHz (-10dB).

• The system’s horizontal coverage shall be 70º, with vertical coverage of 70º.

• SPL, measured at 1W and 1m under free field conditions shall be 92 dB. Maximum SPL continuous, measured at 1m under free field conditions shall be 115 dB. Maximum SPL peak, measured at 1m under free field conditions shall be 118 dB.

• Maximum continuous musical program shall be 200W.

• Enclosure shall be bass-reflex type with one round duct.

• Enclosure cabinet construction shall consist of birch plywood. Dimensions shall be 230 mm (9.05 inch) wide, 400 mm (15.7 inch) high, 250 mm (9.8 inch) deep. Enclosure weight shall be 6.4 Kg.

• Enclosure cabinet finish shall consist of black or white matt high-resistance Polyurea® paint.

• The front enclosure shall be protected by a 1.5mm steel grille with acoustically transparent technical mesh. The grille shall be secured via screws to keep it in place when facing the cabinet downwards.

• The enclosure shall include M8 points for rigging and shall be used in conjunction with dedicated rigging accessories. Rigging accessories shall be affixed with special crop resistant screws.

• Electrical connections shall be made via one of the two 4-pole NL4MP Speakon connectors with the following configuration: +1/-1 signal input, +2/-2 disconnected.

• The system shall include an internal passive crossover.

• The loudspeaker system shall be the Amate Audio® NÍTID S6LP.

• The rigging accessories shall be the Amate Audio® HR-LU, HR-LU/GT, ACR-M8, SP-6N, SP-WHR, RB-S, RB-S/GT.

April 2024